## Slide 1: Simulation Analysis of Machine Breakdown and Repair Efficiency
By: Lizbeth Hernandez, Al Pakrosnis, Mihir Thakkar, Rohan Saini (Best Team)

## Slide 2
Simulate and evaluate the cost of operating a manufacturing system with 3 machines and 2 repairmen over 800 hours, analyzing breakdowns, repair times, and operational efficiency. Calculate the total cost of running the system, including $50 per broken machine and $10/hour per repairman, and assess the cost-effectiveness of adding 1–3 additional machines to minimize production halts. Providing recommendations on whether purchasing more machines improves system performance and reduces overall costs.
Objective

## Slide 3
Random Breakdown & Repair Time:
Machine breakdowns and repair times modeled using exponential distribution (mean breakdown time: 8 hours, mean repair time: 2 hours).
Machine Status:
Each machine's status determined by its operational time and next breakdown time.
Repairmen Status:
Tracked as binary (0: available, 1: busy), ensuring only one repairman works on a machine at a time.
Calculation Details:

## Slide 4
Queue Length:
Monitors wait times for machines awaiting repair when both repairmen are occupied
Cost Calculation:
Total cost = $50 per broken machine + $10/hour per repairman.
Costs updated hourly based on the system's state.
Summary: The system simulation integrates random breakdowns, repair times, machine and repairman statuses, queue length, and cost tracking to evaluate total operational costs over 800 hours. These calculations guide recommendations for improving efficiency by adding machines.
Calculation Details:

## Slide 5
3 Machines: Cost per machine= $20,770
Average queue length = 0.4725
4 Machines: Cost per machine= $27,240
Average queue length = 0.6375
5 Machines: Cost per machine= $38,160
Average queue length = 0.905
6 Machines: Cost per machine= $43,760
Average queue length = 1.045
Results

## Slide 6
Graph 1:
Visuals
Graph 2:
Chart: Total cost and # machines
| 3 | 4 | 5 | 6
total cost | 20770 | 27240 | 38160 | 43760
Chart: 
| 3 | 4 | 5 | 6
Avg Queue Length | 0.4725 | 0.6375 | 0.905 | 1.045

## Slide 7
3 Machines: Lowest cost per machine ($20,770) and shortest average queue length (0.4725). Operational time: 790 hours.
4 Machines: Increased operational time to 798 hours but at a higher cost per machine ($27,240) and slightly longer queue length (0.6375).
5 Machines: Further operational improvement to 798 hours, but cost per machine rose to $38,160 with a queue length of 0.905.
6 Machines: Maximum operational time (798 hours) but with the highest cost per machine ($43,760) and a queue length of 1.045.
We recommend that if the Total Cost increase from 3 machines to 4 machines is less than the revenue lost from the lesser Total Operational Time for 3 machines, then the manufacturer should choose 4 machines.
Conclusion

## Slide 8
As a team we believe that everyone put in a roughly similar amount of effort into the final project.
We are confident in our assessment that everyone was integral in the work, and it is hard to ascertain which specific parts of the presentation was done by one singular person.
Team Collaboration Breakdown